## Slide 1
Simple Machines
Inclined Plane, Wedge, and Screw
© 2012 Project Lead The Way, Inc.
Principles of Engineering

## Slide 2: The Six Simple Machines
Inclined Plane
Screw
Wedge

## Slide 3: Mechanical Advantage (MA)
Ratio of the magnitude of the resistance and effort forces
Ratio of distance traveled by the effort and the resistance force
Calculated ratios allow designers to manipulate speed, distance, force, and function

## Slide 4: Mechanical Advantage Example
Effort force travels 4 times greater distance than the resistance force.
Magnitude of Force
Distance Traveled by Forces
A mechanical advantage of 4:1 tells us
what about a mechanism?
Effort force magnitude is 4 times less than the magnitude of the resistance force.

## Slide 5: Mechanical Advantage Ratios
One is the magic number
If MA is greater than 1:
Proportionally less effort force is required to overcome the resistance force
Proportionally greater effort distance is required to overcome the resistance force
If MA is less than 1:
Proportionally greater effort force is required to overcome the resistance force
Proportionally less effort distance is required to overcome the resistance force
MA can never be less than or equal to zero.

## Slide 6: Ideal Mechanical Advantage (IMA)
Theory-based calculation
Friction loss is not taken into consideration
Ratio of distance traveled by effort and resistance force
Used in efficiency and safety factor design calculations
DR = Distance traveled by resistance force
DE = Distance traveled by effort force

## Slide 7: Actual Mechanical Advantage (AMA)
Inquiry-based calculation
Frictional losses are taken into consideration
Used in efficiency calculations
Ratio of force magnitudes
FE = Magnitude of effort force
FR = Magnitude of resistance force

## Slide 8: Inclined Plane
A flat surface set at an angle or incline with no moving parts
Able to lift objects by pushing or pulling the load

## Slide 9: Inclined Plane IMA
DE = Distance traveled by the effort = L
DR = Distance traveled by the resistance = H
What is the IMA of the inclined plane above?
4.0 ft
15.0 ft
IMA = 15.0 ft / 4.0 ft = 3.75 = 3.8:1

## Slide 10: Inclined Plane AMA
4 ft
15 ft
50 lb
20 lb
What is the AMA of the inclined plane above?
AMA = 2.5 = 2.5:1
What is the efficiency of the inclined plane above?
% Efficiency =
= 67%

## Slide 11: Wedge
Functions as a moving inclined plane
Tapers to a thin edge and is used for splitting, raising heavy bodies, or for tightening by being driven into something

## Slide 12: Wedge IMA
DE = Distance traveled by the effort = L
DR = Distance traveled by the resistance = H
What is the IMA of the wedge shown?
IMA = 10.0 in. / 3.0 in. = 3.33 = 3.3:1
H 3.0 in.
L 10.0 in.
Notes: There is debate about whether the “length” is perpendicular to the height or the length of the sloped surface. Upon research both methods are used and there is little difference in the calculation of IMA with wither measurement. Using two separate formulas and the reason why one formula makes more sense than the other is beyond the scope of this course. If students desire an answer, though, the explanation is below.
Method A - Length is equal to the perpendicular distance to the height (the method used in POE): If the resistance force is constrained such that it can only move perpendicular to the height. i.e. a doorstop.
Method B - Length is equal to slope: If the resistance force moves parallel to the height measurement of the wedge. i.e.

## Slide 13: Wedge AMA
What is the AMA of the wedge shown?
AMA = 2.80 = 2.80:1
What is the efficiency of the wedge shown?
% Efficiency =
= 84%
H 3.0 in.
L 10.0 in.
250. lb
700. lb
700. lb

## Slide 14: Screw
An inclined plane wrapped around a cylinder, forming the path and pitch
A wheel and axle used to create rotary motion
Two Components
Properties
Change rotary motion into linear motion
Used as a threaded fastener
Large MA
Large amount of friction loss

## Slide 15: Screw Identification
Pitch
Effort Arm Distance – If using a wrench, effort arm distance would be the length of the wrench
If 13 threads per inch, then pitch is 1/13 of an inch.
Diameter
Distance between threads and linear distance traveled by 1 rotation of the screw
How far will a screw with 13 threads per inch move linearly if turned one full rotation?
1/13 of a inch
Thread Information
1/2 13 NC
Diameter
Threads per inch
Thread description coarse or fine

## Slide 16: Screw IMA
DE = One rotation of the effort arm = Circumference
DR = Linear distance traveled during one rotation of the effort arm = Pitch
1/4 20 NC
What is the IMA of the screw above if effort is applied by an 8.0in. long wrench?

## Slide 17: Screw AMA
What is the AMA of the screw shown?
AMA = 34.29 = 34:1
What is the efficiency of the screw shown?
% Efficiency =
= 3.4%
8 in.
35 lb
1/4 20 NC
1200 lb
Why is efficiency so low?

## Slide 18: Compound Machines
Simple machines working in combination to complete a task
Calculating mechanical advantage

## Slide 19: Image Resources
Microsoft, Inc. (2008). Clip art. Retrieved January 10, 2008, from http://office.microsoft.com/en-us/clipart/default.aspx